G.E.C Communications Receiver Model MT600

This very much sought after communication receiver, which uses 14 tubes (valves) was first produced in England in 1947, by the General Electric Company. It was designed to be a general purpose communication receiver which would give excellent results, over what was back in 1947, stated to be a wide range of frequencies. The actual frequency range is 150-358kc’s and .51-30Mc’s,in six ranges;150-385kc’s,510-1300 kc’s,1300-3200kc’s,3200-8500 kc’s,8500-20000kc’s and 20000-30000kc’s.Bandspread is by 64 to 1 slow-motion drive and there is a logging scale, divided into 3200 divisions. An attractive feature of this communications receiver is the use of individual edge-lit perspex strips for each range, the range in use being illuminated. The maker’s specified sensitivity is less than 1 microvolt for 1.5 watts output, on all ranges. The IF used is 455kc’s.The receiver has a crystal filter and 6 bandwidths are available;.5,1.0,2.0,5.5,9.0 and 13kc’s.Panel controls on this very collectable communications receiver, are as follows; Tuning, range, aerial trimmer, AF gain, IF gain, RF gain, Selectivity, Crystal Phasing, BFO pitch, Noise limiter, send/receive, Mains on/off, AVC, Audio Filter, Speech/Music switch, BFO on/off. The tube (valve) line-up is a fascinating mixture of old and new types, with many and varied bases,viz.,W81’s,X81,N77,DH81,D63,KT81,Z77’s,KT81,U52 and an enormous but beautiful, S130 stabilizer, which gives off enough warm glow, to light the house! Weight is an impressive 75lbs.This classic piece of receiving hardware, will operate from 95-130 or 195 –250 volts AC.